## Slide 1: A Multirate Field Construction Technique for Efficient Modeling of the Fields and Forces within Inverter-Fed Induction Machines
Dezheng Wu, Steve Pekarek
School of Electrical and Computer Engineering
Purdue University
September 30, 2010

## Slide 2: Motivation for Research
Fields-based modeling of machines valuable analysis tool
  Investigate slot geometries, material properties
  Calculate force vector (radial and tangential)
  Readily model induced currents in magnetic material
Limitation as a design tool
  Numerical computation expensive
Field construction
  Attempt to establish a fields-based model while minimizing computation requirements
  FC of induction machine initially considered by O’Connell/Krein in parallel with Wu/Pekarek

## Slide 3: Field Construction – Basic Idea
Use a minimal number of FEA solutions to characterize machine behavior
  Create basis functions for stator and rotor magnetic fields
‘Construct’ the magnetic field in the airgap using stator field and rotor basis functions under arbitrary current
Bn=Bns+Bnr Bt=Bts+Btr
Calculate torque and radial force using the Maxwell Stress Tensor (MST) method under arbitrary stator excitation and rotor speed

## Slide 4: Assumptions
The flux density in the axial direction is zero
Hysteresis in the iron is neglected
Thermal conditions are assumed constant
No deformation occurs in stator and rotor teeth
Linear magnetics

## Slide 5: Stator Basis Function Derivation
kns
kts

## Slide 6: Rotor Basis Function (knr,ktr) Derivation
Impulse Response
1. Set a discrete-time impulse input to a
transient FEA program
ias(t) = I0 when t = t0
ias(t) = 0 when t ≠ t0
2. Record the flux density components
(Bnid, Btid) for t ≥ t0.
3. Subtract the stator magnetic field
Bnr= Bnid – iaskns , Btr= Btid – iaskts
4. Divided by I0
knr= Bnr / I0 , ktr= Btr / I0

## Slide 7: Complete Characterization Process

## Slide 8: Magnetic Flux Density Due to Stator
The flux density generated by arbitrary stator phase-a current is approximated as
Due to symmetry, the total flux density generated by stator currents

## Slide 9: Magnetic Flux Density Due to Rotor
Obtain rotor magnetic field using the convolution of stator current signal and rotor basis function
where x can be ‘n’ or ‘t’
due to ias
due to ibs
due to ics

## Slide 10: Complete Field Construction – Stator Current as Model Input
Obtain the total flux density in the discrete-time form
In the computer, the discrete convolution of the stator current and rotor basis function
where x can be ‘n’ or ‘t’

## Slide 11: Voltage-Input-Based FC Technique
v  i
Current-input-based FC
i
v
Bn , Bt
Basic idea:
Stator voltage equations are used to relate voltage and current:
where w is the angular speed of an arbitrary reference frame, and the flux linkages are expressed as
Due to the induced rotor current
Unknowns: Lss, Lls, λqs,r, λds,r

## Slide 12: Characterization of Rotor Basis Flux Linkage
Use the same FEA solutions as in the characterization of stator and rotor basis functions.
Impulse response (vector)

## Slide 13: Calculate lqs,r, lds,r
Procedure:
convolution.
transformation between reference frames
where qr is the electric rotor angle, and q is the angle of the reference frame

## Slide 14: Voltage-Input Based FC Diagram
Then iqd0s  iabcs,
and iabcs are then used in the current-input-based FC

## Slide 15: An Induction Machine Fed By An Inverter
A sine-PWM modulation with 3rd-harmonic injection is used. The duty cycles for the three phases are

## Slide 16: Challenges
Wide Range of Time Scales – (Switching Frequency versus Rotor Time Constant)
Resolution of n Hz requires a discrete-time simulation of 1/n second
For a simulation with step size h, the maximum frequency obtained using a discrete-time Fourier transform is 1/(2h)
Total number of sampling steps in the steady state that is required is 1/(nh)
Example:
  Desired frequency resolution is 1 Hz
  Step size is 10 μs
  Total number of simulation steps required in steady state is 100,000.
The large size of rotor basis function and amount of sampling steps add difficulties to computer memory and the computational effort.

## Slide 17: Computational Burden of FC
Dominated by Convolution
Assume Flux Densities are Calculated at p points in the Airgap with N samples

## Slide 18: Multirate Field Construction
In the slow subsystem, FC is used with sampling rate of :
Input  ias,lf , ibs,lf , ibs,lf
Output  Bn,lf , Bt,lf
Low Sampling Reduces Dimension of Convolution Matrix
In the fast subsystem, ‘Fast’ FC is used with sampling rate of :
Input  ias,hf , ibs,hf , ibs,hf
Output  Bn,hf , Bt,hf
Truncate ‘Fast’ Impulse Response at samples
Truncated Impulse Response Reduces Dimension of Convolution Matrix
Indeed Size of the Matrix Nearly Independent of Switching Frequency
Partition Currents into Fast and Slow Components
  Use ‘slow’ impulse response to calculate ‘slow’ component of flux density
  Use ‘fast’ impulse response to calculate ‘fast’ component of flux density

## Slide 19: Multirate Field Construction
High-frequency component ias,hf
Low-frequency component ias,lf
Re-sampling ias

## Slide 20: Example Induction Machine Studied
3-phase 4-pole squirrel-cage induction machine
36 stator slots, 45 rotor slots
Rated power: 5 horsepower
Rated speed: 1760 rpm
rs = 1.2 
Machine parameters | Value
Airgap | 1.42 mm
Rotor outer diameter | 136.92 mm
Stator outer diameter | 228.6 mm
Stack length | 88.9 mm
Shaft diameter | 39.4 mm
Lamination material | M-19
Stator winding material | Copper
Rotor bar material | Aluminum
Number of turns per coil | 22
Number of coils per phase | 6 coils in series connection

## Slide 21: Example Operating Conditions
wrm=1760 rpm
Vdc = 280 V
Sine-PWM modulation with 3rd harmonics injected
Switching frequency = 1 kHz (set low for FEA computation)
Step size of FC = 1 ms (slow subsystem),
0.01 ms (fast subsystem) (oversampled)
Nfast = 100 samples
Bn,lf = O(999 x 10002) calculations/second
Bn,hf = O(999 x 1002) calculations/second
If used Single-rate FC = O(999x1000002) calculations/second
Step size of FEA = 0.01 ms

## Slide 22: Result – Stator Current
FEA ~ 270 hours
FC ~ 48 minutes
ias
Frequency spectrum of ias
fsw-2fe
fsw+2fe
fsw-4fe
fsw+4fe

## Slide 23: Result -- Torque
Torque
Frequency spectrum of Torque
fsw-3fe
fsw+3fe

## Slide 24: Conclusions
Method to efficiently model fields and forces in inverter-fed induction machines presented
  Requires Minimal FEA Evaluations (at Standstill)
Multi-rate Leads to Relatively Low Computation Burden
  Does Not Increase with Switching Frequency
Can be Applied to Flux Density Field Construciton in Iron, i.e. Calculate Core Loss
Requires a Partition of Time Scales

## Slide 25: Acknowledgement
This work is made possible through the Office of Naval Research Grant no. N00014-02-1-0623.